CELT Technical Note No.  5

CELT Segment Positioning Actuators  - Requirements

Jerry Nelson

March 2001

Number of Actuators

The current segmentation calls for 1080 segments

plus  (1080 / 6 = ) 180  spare segments.

Three actuators per segment are used to control piston/tip/tilt of the segment.;  3 * ( 1080 +180) = 3780 + spares   ~ 4000 actuators.

Each actuator connects to the segment through a whiffletree

used to more uniformly distribute the load to the segment.

Requirements (Keck actuators are shown for comparison)

Keck				CELT

Range					> 0.6 mm			> 1.2 mm

Rms position error averaged over 20 min

< 20 nm			< 7 nm

Tracking rate			         2 to 10 moves / sec

Slew rate					> 10  / sec		> 10  / sec

Transverse load capacity 		> 14 kg			> 5 kg

Axial load capacity 			> 150 kg			> 30 kg

Axial stiffness				 > 5.9 x 107 N/m		> 1 x 107 N/m

(~100 Hz resonance)

Transverse stiffness		 	> 12.7 x 105 N/m	> 1 x 105 N/m

Local ave power dissipation		< 10 W			< 2 W

Lifetime	  						ten  ~ 30 nm moves / sec

continuously for 10 years

Survival temperature							2 ±20 oC

Operating temperature 						2 ±8 oC

Operating humidity						0 to 100% condensing

Electrical shock resistance						yes

Dust protected								yes

Easy Installation and Removal 					yes

Budget Goal

Less than   ~ $2000 / actuator including electronics and cabling